## Slide 1
Design of Intelligent Edge and Time-Series Data Flow Temperature Control System
Разработка интеллектуальной системы управления температурой
на основе периферийных вычислений и потоковой обработки временных рядов
Student / Студент: Wang Gen
Руководитель: В.С. Разумейчик
Department / Кафедра: «ЭВМ и систем»
BrSTU / БрГТУ
2026

## Slide 2
Objective And Implemented Scope
Objective
Build an end-to-end prototype for intelligent temperature control.
This work covers system design, software implementation, and prototype validation.
Implemented Scope
1
Edge-side real-time control
Local closed-loop behavior
2
MQTT-based telemetry flow
Continuous device reporting
3
Time-series data storage
Historical query and analysis
4
HMI monitoring and operation
User-facing observation and control
5
AI-assisted PID tuning
Decision support for parameter adjustment
02 / 10

## Slide 3
Requirements And Design Goals
Functional Requirements
• Temperature acquisition and control
• Telemetry upload and storage
• Historical query and visualization
• Alarm and parameter management
• AI-assisted recommendation
Design Goals
Safety
Observability
Traceability
Maintainability
The design focuses on controlled operation, visible runtime behavior, recorded actions, and maintainable system structure.
03 / 10

## Slide 4
End-to-End Closed Loop Architecture
Edge Device
MQTT Telemetry
Data Hub
Time-Series Storage
HMI And AI
Post-Apply Evaluation
Edge ACK
Parameter Update
Human Confirmation
Key Principles
Real-time control remains on the edge.
AI supports PID tuning decisions, not direct actuation.
04 / 10

## Slide 5
Edge Control And Hardware Design
Sensor
Acquisition
Control
Tick
PWM
Output
Local Safety
Priority
Telemetry
+ ACK
Edge Responsibilities
• Sensor acquisition
• Periodic control tick
• PID-compatible parameters
• PWM actuator output
• Output limiting and anti-windup
• Local safety handling
• Parameter ACK
05 / 10

## Slide 6
Telemetry And Control Metrics
Telemetry
• Temperature / setpoint / error
• Control output
• PID parameters
• Device status and fault state
• Timestamp and device ID
Control-quality
features
Control Metrics
• Mean absolute error
• Overshoot
• Settling time
• In-band ratio
• Temperature swing
• Saturation ratio
Telemetry is used for display, control-quality evaluation, and AI feature extraction.
06 / 10

## Slide 7
Data Hub Reliability
MQTT
Validation
Filtering
Queue
Aggregation
Storage
Metrics
Processing Responsibilities
• MQTT telemetry ingestion
• JSON parsing and validation
• Abnormal data filtering
• Bounded asynchronous processing
Storage And Observation
• Short-term aggregation
• TDengine time-series storage
• PostgreSQL management data
• Runtime throughput, latency, and failure metrics
07 / 10

## Slide 8
Hybrid AI-Assisted PID Tuning
AI Role
• Decision support for PID tuning
• Not direct temperature control
• Human-confirmed parameter update
Rule-Based Layer
• Telemetry feature extraction
• Control problem diagnosis
• Conservative PID candidate generation
ML Model Layer
• Candidate PID ranking
• Improvement probability estimation
• Preview risk estimation
• Rule fallback if artifacts are unavailable
1. Telemetry Window
2. Feature Extraction
3. Problem Diagnosis
4. PID Candidates
5. ML Ranking
6. Preview
7. Human Confirm
8. Evaluate
Models: Logistic Regression / Random Forest Artifacts: joblib
08 / 10

## Slide 9
Deployment And Validation
Deployment
• Edge firmware
• MQTT broker
• Java Data Hub
• TDengine / PostgreSQL
• HMI and AI services
Validation
• End-to-end telemetry flow
• Parameter update with ACK
• Data Hub pressure testing
• Baseline throughput and latency
• Metrics and database maintenance
09 / 10

## Slide 10
Results, Limitations And Future Work
Main Results
• End-to-end prototype implemented
• Edge control and telemetry upload verified
• Data Hub ingestion, storage, and metrics verified
• HMI monitoring and parameter management verified
• AI-assisted PID tuning workflow verified
Limitations
• Prototype-level validation
• More physical thermal-load experiments are needed
• Long-term quantitative control evaluation should be extended
Future Work
• Broader device and scenario testing
• Improved adaptive tuning
• Stronger deployment automation and monitoring
The work combines design, implementation, and prototype validation.
10 / 10